## Slide 1: Percolation of information in an ergodic robotic network

## Slide 2: Motivation
Ergodicity: The total visitation frequency of each region is proportional to the noise of observation
Swarm ergodicity requires all robots to have the same information about the regions
  Previously done by central information processing
  Decentralize by locally sharing collected information
How to maintain ergodicity

## Slide 3: Recap
Each region has a state to be estimated
The robots can make a noisy observation when they transition to the region
The estimation of is done by recursive Baye’s law
If the robot starts with the same prior and knows all , then all robot has the same posterior
Mean and variance can be recovered from the posterior
posterior
Likelihood
prior

## Slide 4: Communication Protocol
Samples can be reduced to sufficient statistic
  e.g. mean and variance for gaussian
  Significantly reduce memory and communication
Each robot keeps a list of from the other robots
When they communicate, they acquire the most recent in their entire list from each other
The robots communicate IFF they are in the same region
 | Robot 1 | Robot 2 | Robot 3
Robot 1 |  |  | 
Robot 2 |  |  | 
Robot 3 |  |  | 
 | Robot 1 | Robot 2 | Robot 3
Robot 1 |  |  | 
Robot 2 |  |  | 
Robot 3 |  |  | 

## Slide 5: Problem Formulation
Assume every robot has a fixed initial piece of information
All robot has the same probability distribution of existing in the regions
How many time step can we expect all the initial information is shared to every robot?
Conjecture:
there is a sharp time step where the information is almost certainly shared across the robot network (as the number of robot tends to infinity)

## Slide 6: Pictorial Representation
temporal graph
k=1
k=2
k=3
Robot 1
Robot 2
Robot 3
Robot 4
Acquired
Acquired
Acquired
Missing

## Slide 8: Percolation Theory
Historically: a study of how fluid flow through porous material in statistical mechanic
  e.g. water passing through coffee grounds
In mathematics: A study of change of connectivity by adding random link in a graph
Often shows critical phenomenon
  A sudden change in behaviour when a parameter pass the critical point as it is being smoothly varied
  e.g. ising model (magnets) , Erdős–Rényi model (random graph), phase change (boiling water)

## Slide 9: Information Percolation
Does the information show critical phenomenon
  Is there a critical time window where all information is guaranteed to be shared to all robot
  i.e. there exist a path from all nodes to all nodes in the temporal graph
How to model the critical time window
  Given that the number of robots are known and the robots travel in the regions ergodically
  Solution: Absorbing Markov chain

## Slide 10: Simulated Result
Key results:
  Critical phenomenon exists
  The more robots, the sharper the phase change is
  The more robots, the smaller the critical time window is
Setting:
10 regions E-R graph
Uniform distribution
1000 trials
REMC transition law

## Slide 11: Mean Field Approximation
Popular method for handling statistic problem with large amount of variables
  e.g. Ising model, Navier-Stokes, pandemic modelling
Treat the swarm as continuous variables and approximate the dynamic using expected value
  E.g. it is possible to have 1.53 robot in a region

## Slide 12: Mean Field Approximation - Formulation
Only consider single source for now
Define the proportion of robot that has the information as
  The rest is
At any time if a region has at least 1 informed robot, the rest will also become informed, the expected increase of informed robot is
Probability of at least one informed robot in the region
Expected number of uninformed robot in the region
Solve the difference equation
Only 1 informed robot out of N initially

## Slide 13: Markov Chain Formulation
Consider the number of informed robot as a state
Every time step, after the robot moved, there is a chance of the numer of informed robots increasing (transition to subsequent state) or stays constant (self loop). But never decrease (go back to previous states)
Eventually the chain terminates at all robots being informed
  This is called an absorbing chain
IMPORTANT: this Markov chain is not related to the ergodic Markov chain
1 informed robot
2 informed robot
N informed robot

## Slide 14: Expected Absorption Time
The corresponding stochastic matrix is
The expected absorption time is given by
Need to find the expression for (probability of informed robot increased from r to n in 1 step)
  significantly easier than direct method (but still hard)
    Mean field approx?
Not scalable with a lot of robots (inverting (N-1)X(N-1) matrix)
Need to formulate as multi-source percolation

## Slide 15: First Hitting Time Method (fully connected)
How many way to get r uninformed robots
r robots meet with at least 1 informed robots
Rest of the uninformed robot does not meet with any informed robot
Pairwise meeting chance
(fully connected)
Initial distribution
Probability of not absorbed in k step
Pairwise approximation
(accurate if meeting chance is not too high)

## Slide 17: Pairwise Meeting Chance on Region Graph
Consider 2 agents on a region graph with a given transition matrix
Create new state space with the cartesian product
Find initial state in combined state space
Remove “collision states”
1
2
Region graph
1,1
1,2
2,1
2,2
Cartesian product
(1,1)
(1,2)
(2,1)
(2,2)
Initial distribution

## Slide 19: Conditional Pairwise Meeting Chance
We need the conditional meeting chance
  Given that the robot never met an informed robot, what is the chance of meeting an informed robot in the next step
1s at collision states
Space distribution never met from 0 to k-1
(Probably can be simplified)
Interesting effect: the longer K is, the lower this probability is, but approach a fix value for very big K
Interpretation: if they haven’t meet in a long time, they probably are initially very far away in the region graph

## Slide 20: Time varying first hit model
Original first hit model
Time varying first hit model

## Slide 21: Region-aware absorbing chain
1 informed robot
2 uninformed robot in region 1,
1 informed robot in region 2
2 informed robot
3 informed robot
Expand nodes to sub-graphs

## Slide 22: 1 robot getting informed in 1 step
Uninformed
meet
informed

## Slide 23: Statistical mechanics 1
Probability of configuration
Multinomial Distribution
Total probability of not meeting =
Probability of no robot in region
Probability of non-meeting configuration
Transition probability from
Flux matrix
Total probability of meeting =
No robot transition to region j =
Not meet (given n,i) =
Number of configuration =
Not meet (given n) =

## Slide 24: Statistical mechanics 2
Not meet at 1 (given n)
Not meet at 1 (given not meet at 0, )
Total probability of not meeting at 0 =
Not meet at 1 (given not meet at 0, n)
Not meet at 1 (given not meet at 0)
Not meet at 1 (given not meet at 0)

## Slide 25
If rho0 = pi

## Slide 26: Generalize
Given find combined initial vector
Partition to state of robot 1 being with other informed robots (informed state) and not being with other informed robots (uninformed state)
Informed probability is the flux ratio from uninformed to informed
Given find compound transition
Where

## Slide 27: Independent approximation